FU TEN DUO INDUSTRIAL CORP.

Automatic blow molding machine (Air system)

This machine can continue ingenuity and innovation, so speed fast, can use different material (for example:PP,PE,PVC,EVA and PS) produce any kind of plastic product, for example liquid medicine bottles, toys, pepeycles, most economic, and most good condition machine.

| Model | FTD-640 | FTD-640E |
| --- | --- | --- |
| Material to be used | PE/PP, PVC | PE/PP, PVC |
| L/D | 1:22 | 1:22 |
| Driving Motor | VS 3HP, VS 5HP | VS 3HP, VS 5HP |
| Max Extruder Capacity/Per Hour | 15 KG | 15 KG |
| Heating Zone(Barrel) | 2 Point | 2 Point |
| Heating Capacity(Barrel) | 2.7 KW | 2.7 KW |
| Die Head | Max Dia of Die | Ø40 MM | Ø40 MM |
|  | Heating Zone | 1 Point | 1 Point |
|  | Heating Capacity | 0.6 KW | 2 KW |
| Mould Plate | Max Open Stroke | 230 MM | 70 MM |
|  | Min Close Stroke | 70 MM | 230 MM |
|  | Mold Length | 80 mm ~ 330 mm | 80 mm ~ 330 mm |
| Product | Dia Max | Ø80 MM | Ø80 MM |
|  | Dia Min | Ø10 MM | Ø10 MM |
|  | Capacity Max | 400 CC | 400 CC |
|  | Capacity MIN | 20 CC | 20 CC |
|  | Weight Max | 32 G | 32 G |
| Total Power Consumption | 10 KW | 11 KW |
| Weight of Machine | 750 KG | 1000 KG |
| Packing Size (L x W x H) | 2.4x1.1x1.9(M) | 2.4x1.1x2.0(M) |
| Machine Measement M³ | 4’ | 4.5’ |

All specification and design are subject to change without notice.