FU TEN DUO INDUSTRIAL CORP.

# Automatic Blow Molding machine/Single head, Single station.

# Specially designed hydraulic circuit allows two speeds of mold traverse for accurate mold positioning.

# Extruder in special structure for automatic upward-downward moving unit.

# High plasticizing capacity extrusion screw is designed to handle material variations.

We develop these machines with regard to the characteristics of the materials (i.e. PVC, PC, PP, PE, K RESIN, EVA etc.)

The material is unable to oxidize, the quality of products is stable,the die head is easy and quick to clean the over materials.

| Automatic Blow Molding machine/Single Head, Single Station. |
| --- |
| BASIC SPECIFICATION | Model NO. | FTD-645S | FTD-655S | FTD-665S | FTD-675S |
|  | Material: | PP/PE, PVC | PP/PE, PVC | PP/PE, PVC | PP/PE, PVC |
|  | Product Min/Max Cap. | cc | 50~1000 | 150~2500 | 500~5000 | 5000~15000 |
|  | Product Min/Max Dia. | mm | 20~110 | 30~150, 30~140 | 50~220 | 150~260 |
|  | Product Weight | g | 10~100, 15~65 | 20~170, 30~110 | 40~280, 45~210 | 40~260 |
|  | Extruding Mouth Outer Dia. | mm | 80, 60 | 100, 80 | 140,120 | 200 |
|  | Dry Cycle | Sec. | 3.4 | 3.6 | 3.8 | 5 |
|  | Max Extrusion Capacity | kg/hr | 22, 25 | 33, 38 | 45, 48 | 70 |
| EXTRUSION SYSTEM | Screw Diameter | mm | 45 | 55 | 65 | 75 |
|  | L/D Ratio | L/D | 22/1 | 22/1 | 22/1 | 22/1 |
|  | Screw Rotating speed | r.p.m | 20~60, 20~50 | 20~60, 20~50 | 20~60, 20~50 | 20~60 |
|  | Extruding VS Motor | HP | 10, 15 | 15, 20 | 20, 25 | 25 |
|  | Number of Heaters | Zone | 5, 6 | 5, 6 | 6 | 6 |
|  | Heating Capacity | KW | 6.8, 8.5 | 9.4, 11 | 10, 12 | 20.2 |
| MOULD SYSTEM | Max/Min opening stroke | mm | 80~320 | 90~410 | 90~550 | 160~700 |
|  | Mould clamping force | Ton | 2.6 | 3.3 | 4.8 | 13.3 |
|  | (Max) Mould Dimension | mm | 280x320 | 300x380 | 330x420 | 540x800 |
| HYDRAULIC SYSTEM | Hydraulic pump power | HP | 7.5 | 7.5 | 10 | 10 |
|  | Air Pressure | kg/cm² | 5~6 | 5~6 | 5~6 | 5~6 |
|  | Air compressor | HP | 3 | 5 | 5 | 7.5 |
|  | Oil tank capacity | gallon | 70 | 90 | 110 | 120 |
|  | Electricity consumption | KW | 18.6, 21 | 27.4, 32.5 | 31.5, 44.5 | 46 |
| PACKING | Net weight | Ton | 2.8 | 3.2 | 4 | 6 |
|  | Machine size | M | 2.1x1.7x2.3 | 2.5x1.8x2.6 | 2.8x2.0x2.8 | 3.3x2.3x2.6 |
|  | Packing size | M | 2.2x1.8x2.1 | 2.6x1.9x2.4 | 2.9x2.1x2.6 | 3.4x2.3x2.3 |

All specification and design are subject to change without notice.