FU TEN DUO INDUSTRIAL CORP.

Visible Stripe (Window) Automatic Blow Molding machine/Single head, Two layer

- User-friendly LCD control panel with auto memory for mold production program.

- Password programmable.

- Error display to enable rapid trouble-shooting.

These series have multi-functions for different products, such as visible stripe for motor oil, toys with two colors, and high quality bottles with two layers (cosmetic, shampoo bottles etc.) It also can produce the bottles with three layers, depending on the requirement of the customers.

| Automatic Blow Molding machine/Single head & Two Layer, Visistrip (Window) |
| --- |
| BASIC SPECIFICATION | Model NO. | FTD-645SL | FTD-655SL | FTD-665SL |
|  | Material: | PE/PP | PE/PP | PE/PP |
|  | Product Min/Max Cap. | cc | 50~1000 | 150~2500 | 500~5000 |
|  | Product Min/Max Dia. | mm | 20~110 | 30~150 | 50~220 |
|  | Product Weight | g | 10~100 | 20~170 | 40~280 |
|  | Outer Dia.of Extruder | mm | 80 | 100 | 140 |
|  | Dry Cycle | Sec. | 3.4 | 3.6 | 3.8 |
|  | Max Extrusion Capacity | kg/hr | 22 | 33 | 45 |
| EXTRUSION SYSTEM | Screw Diameter | mm | Ø45, Ø25 | Ø55, Ø25 | Ø65, Ø25 |
|  | L/D Ratio | L/D | 22/1 | 22/1 | 24/1 |
|  | Screw Rotating speed | r.p.m | 20~60 | 20~60 | 20~60 |
|  | Extruding VS Motor | HP | 10, 3 | 15, 3 | 20, 3 |
|  | Number of Heaters | Zone | 5, 2 | 5, 2 | 6, 2 |
|  | Heating Capacity | KW | 6, 2.3 | 9.4, 2.3 | 10, 2.3 |
| MOULD SYSTEM | Max/Min opening stroke | mm | 90~410 | 90~550 | 160~660 |
|  | Mould clamping force | Ton | 3.5 | 4.8 | 12 |
|  | (Max) Mould Dimension | mm | 300x380 | 300x420 | 550x540 |
| HYDRAULIC SYSTEM | Hydraulic pump power | HP | 7.5 | 7.5 | 10 |
|  | Air Pressure | kg/cm² | 5~6 | 5~6 | 5~6 |
|  | Air compressor | HP | 3 | 5 | 5 |
|  | Oil tank capacity | Gallon | 70 | 90 | 110 |
|  | Electricity consumption | KW | 24.3 | 30.7 | 35.2 |
| PACKING | Net weight | Ton | 2.8 | 3.2 | 4.2 |
|  | Machine size | M | 2.3x1.7x2.3 | 2.7x1.8x2.6 | 3.0x2.1x2.8 |
|  | Packing size | M | 2.4x1.8x2.4 | 2.8x1.9x2.7 | 3.1x2.2x2.9 |

All specification and design are subject to change without notice.