FU TEN DUO INDUSTRIAL CORP.

EVA (TPR) Pelletizing Plant 強力加壓利拿式捏合造粒成型整廠設備

EVA /TPR/PVC橡膠及色母造粒整廠設備

Wter-Ring-Cutting Kneader Extruding Plant (EVA、Rubber、TPR)

Fan-Cooling-Cutting Kneader Extruding Plant (EVA、Rubber、TPR)

Spot:

- can mix with the every kind of chemistry raw material formulation, produce various plastics grain.

- crain admixtrue the degree is very average, the grain degree size is even to make uniform.

- per hour manufacturing plastics grain ability is very strong, save time and again a province manpower.

- produce get dintr assistant.

| TYPE | FTD-65 | FTD-85 | FTD-100 | FTD-120 | FTD-165 |
| --- | --- | --- | --- | --- | --- |
| Main Stalk Dia. | Ø65mm | Ø85mm | Ø100mm | Ø120mm | Ø165mm |
| Screw Length L/D | 10/1 | 10/1 | 10/1 | 10/1 | 10/1 |
| Drive Motor | 10HP-AC Inverter | 30HP-AC Inverter | 50HP-AC Inverter | 60HP-AC Inverter | 100HP-AC Inverter |
| Productivity kg/hr | 15 | 80~150 | 120~200 | 200~300 | 300~450 |
| Kneader force | 2HP | 5HP | 7.5HP | 7.5HP | 10HP |
| Rotate Speed | 35RPM |
| Auto thermo Controller | 3 Zones | 4 Zones |
| Barrel Cooling Device | Water Cooling |
| Granular Diameter | 3~5 mm |
| Pelletizing Motor | 1HP | 2HP | 2HP | 2HP | 3HP |
| Cooling Device | Air Cooling or Water Cooling |
| Gear Box | Oil Bath Lubrication |
| Speed Variation | 1 St Step-Freq. W.V. OR 2Nd Step |
| Blower Motor | 1HPx3” | 3HPx4” | 3HPx4” | 3HPx4” | 5HPx5” |
| Cooling Barrel | 2 sets | 2 sets | 2 sets | 2 sets | 2 sets |
| Storage Barrel Capacity | 200 kgs | 400kg(臥) or 200(立) | 600 kgs | 600 kgs | 1000 kgs |
| Machine Size | L265xW81xH130cm | L310xW165xH160cm | L335xW180xH195cm | L380xW180xH195cm | L480xW195xH205cm |
| Machine N.W. | 1500 kgs | 2000 kgs | 2500 kgs | 3000 kgs | 4000 kgs |

This catalogue is for order reference only. Designs and specifications are subject to change without notice.