FU TEN DUO INDUSTRIAL CORP.

Rubber/Plastic Calender : Three Roll Calender : Common Bed Type/Vertical

Used for making rubber sheets and for coating or friction one side of tire cord with rubber.

Specification:

| Model Size of Rolls Horse Power FTD-907-1 Ø8” x 24”L 15HP FTD-907-2 Ø10” x 30”L 25HP FTD-907-3 Ø12” x 36”L 40HP FTD-907-4 Ø14” x 42”L 50HP FTD-907-5 Ø16” x 48”L 75HP FTD-907-6 Ø18” x 54”L 100HP FTD-907-7 Ø22” x 66”L 150HP FTD-907-8 Ø24” x 72”L 200HP | Also Product ※Rubber/Plastic Calender Two Roll Calender/Common Bed type/Vertical *Used for making PVC floor tile or automatic tire, footwear etc. ※Rubber/Plastic Calender Four Roll Calender/Common Bed type |
| --- | --- |

|  | MIXING ROLL Machinery Direct Type Item No.: FTD-102B |
| --- | --- |
| Size Per batch Capacity Motor machine size (cm) N.W.(ton) approx Masstication Mixing L W H Ø16”x42”L(406mmx1067mm) 18kg 40kg 50HP 490 168 130 8.4ton Ø18”x48”L(457mmx1219mm) 27kg 60kg 75HP 595 184 145 12ton Ø22”x60”L(559mmx1524mm) 45kg 100kg 125HP 670 204 155 18.5ton Ø24”x72”L(610mmx1830mm) 75kg 160kg 150HP 740 283 170 26.5ton |

|  | MIXING ROLL Machinery BELT Type Item No.: FTD-101A |
| --- | --- |
| Size Per batch Capacity Motor Machine Size(cm) N.W. (ton) approx Masstication Mixing L W H Ø12”x30”L(305mmx762mm) 8kg 40kg 50HP 490 168 130 8.4 Ø14”x36”L(350mmx914mm) 12kg 60kg 75HP 595 184 145 120 Ø16”x42”L(405mmx1067mm) 18kg 100kg 125HP 670 204 155 18.5 Ø18”x48”L(457mmx1219mm) 27kg 160kg 150HP 740 283 170 26.5 |