M.C.TYPE CYLINDRICAL-INTERNAL&EXTERNAL HYDRAULIC 油壓式內外圓磨床

## GRINDING MACHINES

| MODEL型式 SPECIFICATION規格 |  | M.C ETH-400 ETH-600 | M.C ETH-650 ETH-1000 | M.C ETH-1500 ETH-2000 |
| --- | --- | --- | --- | --- |
| CAPACITY 能量 | DISTANCE BETWEEN CENTERS兩頂心間距離 | m.m. | 400/600 | 650/1000 | 1500/2000 |
|  | MAX.GRINDING DIAMETER工作最大直徑 | m.m. | φ260(φ300) | φ300(φ400) | φ400 |
|  | HYDRAULIC TANK-CAPACITY油壓油箱 | L | 50 | 60 | 80 |
|  | COOLANT TANK-CAPACITY冷卻水箱 | L | 70 | 100 | 100 |
| TABLE 床台 | TRAVERSE SPEED床台速度 | mm/MIN | 75-3000 | 50-2500 | 50-2000 |
|  | TRAVEL PER HANDWHEEL ROTATION手輪進給 | mm/REV | 13 | 13 | 10 |
|  | SWIVEL ANGLE-CLOCKWISE旋轉角度工作者邊 | ° | 12/0 | 3/0 | 4/3 |
|  | SWIVELANGLE-COUNTER CLOCKWISE 旋轉角度砂輪邊 | ° | 7/12 | 10/9 | 8/6 |
| HEADSTOCK 主軸台 & TAILSTOCK 尾座 | HEADSTOCK WORK CENTER主軸台頂針 | M.T | NO.4 | NO.4(NO.5) | NO.5 |
|  | TAILSTOCK WORK CENTER尾座頂針 | M.T | NO.3 (NO.4) | NO.4 | NO.5 |
|  | WORKHEAD SWIVEL ANGLE-CLOCKWISE 工作者邊 | ° | 30° | 30° | 30° |
|  | WORKHEAD SWIVEL ANGLE-COUNTER CLOCKWISE砂輪邊 | ° | 90° | 90° | 90° |
|  | WORKHEAD SPINDLE SPEED工作主軸轉速 | R.P.M | 100-362 | 20-100,60-380 | 20-100,60-380 |
| WHEELHEAD 砂輪台 | GRINDING WHEEL SPINDEL SPEED砂輪轉速 | R.P.M | 2085,2495 | 1530,1800 | 1310,1540 |
|  | GRINDING WHEEL SIZE(OD.×WIDTH×ID.) 砂輪直徑 | m.m. | φ400×25-32×φ127 | φ450×38-50×φ127 | φ510×50-75×φ203.2 |
|  | IN-FEED PER GRADUATION OF HANDWHEEL(φ) 每一微分進給(直徑) | m.m | 0.005 | 0.005 | 0.005 |
|  | IN-FEED PER REVOLUTION OF HANDWHEEL(φ) 手輪每轉進給(直徑) | m.m/REV | 2 | 2 | 2 |
|  | RAPID IN-FEED STROCK (M.C)快送行程 | m.m/MIN | 40 | 40 | 40 |
|  | GRINDING WHEEL SWIVEL砂輪頭角度 | ° | ±30 | ±30 | ±30 |
|  | INTERNAL GRINDING WHEEL SPINDLE SPEED 內孔研磨主軸轉速 | R.P.M | 14000,18000,20000 | 14000,18000,20000 | 14000,18000,20000 |
| ELECTRIC MOTORS 馬達 | WHEEL DRIVE MOTOR 砂輪馬達 | K.W. | 3.7(4P) | 5.5(4P) | 7.5(4P) |
|  | WORK SPINDLE MOTOR工作台馬達 | K.W. | 0.4 | 0.75 | 1.5 |
|  | HYDRAULIC PUMP MOTOR油壓馬達 | K.W. | 0.75 | 1.5 | 2.25 |
|  | WHEEL SPINDLE LUBRICATOR MOTOR 砂輪潤滑馬達 | K.W. | 0.2 | 0.2 | 0.4 |
|  | COOLANT PUMP MOTOR 冷卻泵馬達 | K.W. | 0.1 | 0.2 | 0.2 |
|  | SLIDE WAYS LUBRICATOR MOTOR床軌潤滑馬達 | K.W. | 0.1 | 0.1 | 0.1 |
|  | SURFACE REQUIRED 機械裝置空間 | m.m. | 1750×1850/2170×1950 | 2260×2050/3020×2050 | 5050×2250/6050×2250 |
|  | NET WEIGHT機器重量(約) | KGS | 2000/2100 | 2800/3700 | 5200/6200 |

STANDARD MODELS:						標準機型:

1. M: AUTO TABLE TRAVERSE & MANUAL INFEED	工作台左右自動，砂輪頭手進給

2. C: AUTO TABLE TRAVERSE & AUTO INFEED WITH SPARKOUT GRINDING 工作台左右自動，砂輪頭自動進給

STANDARD ACCESSORIES:					標準附件:

1. SWIVEL BASE MOTOR-DRIVEN WORKHEAD     旋轉式主軸台

2. LEVER-OPERATED TAILSTOCK				尾座

3. WORKHEAD& TAILSTOCK CENTERS			主軸台及尾座頂針

4. STANDARD GRINDING WHEEL				標準砂輪

5. WHEEL FLANGE AND EXTRACTOR			砂輪法蘭及拆卸器

6. WHEEL DRESSER HOLDER					砂輪修整儀

7. COOLANT SUPPLY UNIT					冷卻水裝置

8. LUBRICANT SUPPLY UNIT					潤滑油裝置

9. TABLE SWIVEL INDICATOR					床台旋轉校錶裝置

10. SPLASH GUARD							防水板

11. DIAMOND DRESSING TOOL					鑽石刀

12.TOOLS AND TOOL BOX					手工具

ADDITIONAL EQUIPMENTS:					特殊附件:

1. INTERNAL GRINDING ATTACHMENT   		內孔研磨裝置

2. 3-POINT STEADY REST						三點式穩定扶架

3. 2-POINT STEADY REST						兩點式穩定伏架

4. 3-JAW SELF-CENTERING CHUCK AND PLATE 	三爪夾頭及面盤

5. 4-JAW INDEPENDENT CHUCK AND PLATE    	四爪夾頭及面盤

6. PERMANET MAGNETIC CHUCK AND PLATE  	永久磁鐵及面盤

7. MAGNET COOLANT FILTER                  	磁性冷卻除屑裝置

8. RADIUS WHEEL DRESSER                    	圓弧砂輪修整機

9.ANGULAR WHEEL DRESSER                 	角度砂輪整修儀

10. WHEEL BALANCING UNIT					砂輪平衡儀

11. EXTRA GRINDING WHEEL                   	備用砂輪

12. EXTRA WHEEL FLANGE  					備用砂輪法蘭

13 EXTRA DIAMOND DRESSING TOOL			備用鑽石刀

(本公司保有變更規格設計權利不需另行通知)

(The company reserves the right to change specifications and design of its machine without any prior notices.)