| 32Inch LCD TV SPECIFICATION |
| --- |
| Type | Item | Spec |
| LCD panel | LCD panel specification for reference only! |
|  | Panel brand | CMO |
|  | Solution | Mstar9E19 |
|  | Screen size | 32” TFT-LCD panel |
|  | Aspect ratio | 16:9 |
|  | Resolution | 1366*768 |
|  | Viewing angle | 170º (H); 170º (V) (Typical) |
|  | Brightness | 420cd/m2 (Typical) |
|  | Contrast ratio | 1000:1 |
|  | Response time | 8ms |
| Video System | Comb filter | 3D |
|  | Analog video format | PAL/Secam/NTSC |
| Audio System | Speaker system details | 2 x 10Watt Right/Left channel speaker |
|  | Sound mode | Flat/Sport/music/movie/user |
|  | Audio controls | Bass, Treble, Balance |
|  | Audio Stereo | A2, Nicam (Europe only), Stereo, Mono, BTSC |
| Television Features | Display menu language | English-French-German-Italian- Russian (can be added) |
|  | Picture mode | Standard/Dynamic/Mild/User/Game |
|  | Screen mode | 16:9/4:3/14:9 |
|  | PIP | YES |
| TV tuner/ Channel Details | TV tuner reception system | PAL/SECAM/NTSC (Option) |
|  | Stereo reception system | B/G, D/K, I, L’, L, M, N |
|  | TV tuner channel | 200 |
|  | DBX noise reduction | YES |
|  | Teletext | 100pages(Europe Only) |
|  | HDTV Ready | 1080i, 720p |
| IN/OUT Connections | ANTENNA-in | 1 |
|  | Earphone out | NO |
|  | S-VIDEO | 1 |
|  | AV-IN | 1 |
|  | Audio-in | 1 |
|  | Audio-out | NO |
|  | Scart Jack | 1 (Europe Only) |
|  | VGA IN | 1 |
|  | PC audio-in | 1 |
|  | HDMI | 1 |
|  | YUV (Y/Cb/Cr) | 1 |
| Power | Power Supply | AC 100V-240V 50/60HZ |
|  | Working Consumption | ≤180W(max) |
|  | Standby | ≤3W |
| Packing | Packing size | 920*693*260MM |
|  | Weight (G.W./N.W) | 15.6kgs/18.43KGS |
|  | Container (20/40GP/40HQ) | 172/367/401pcs |
|  | Containe r(Pallet) (20/40GP/40HQ) |  |